## Slide 1
Lysosomes Detector GUI
Automated 3D Lysosome Detection
Cell Segmentation
Quantitative Fluorescence Analysis

## Slide 2
Why this software?
Problems:
• Manual counting
• Observer bias
• Time-consuming
Solution:
• Automated detection
• Cell assignment
• Quantification
• Publication-ready outputs

## Slide 3
Software Overview
GUI
Image Loader
Detection
Segmentation
Quantification
Export

## Slide 4
Complete Workflow
Input
Metadata
Gaussian
LoG
Radius
Watershed
Assign
Quantify
Export

## Slide 5
GUI Overview
Image
Parameters
Results

## Slide 6
Image Loading & Metadata
📁 Input Image
TIFF / OME-TIFF / CZI
🔍 Read Metadata
Extract voxel size and image dimensions
📏 Physical Pixel Size
X, Y and Z spacing (µm)
❓ Metadata Missing?
Prompt user to enter voxel size manually
✅ Ready for Processing
Validated image and metadata
Purpose
• Supports multiple microscopy formats
• Automatically extracts voxel metadata
• Requests manual values only when needed
• Ensures accurate physical measurements

## Slide 7
Image Preprocessing
Raw Image
Original fluorescence stack
Normalization
Intensity scaling
Gaussian Smoothing
Noise suppression
Background Correction
Remove low-frequency background
Preprocessed Image
Optimized for LoG detection
Why preprocess?
• Improve signal-to-noise ratio
• Reduce false detections
• Enhance blob detection
• Increase segmentation robustness

## Slide 8
Lysosome Detection
blob_log identifies candidate lysosomes in the 3D volume.
LoG
Blob Candidates
Threshold
Coordinates
Detected

## Slide 9
Radius Refinement
3D Gaussian Fit
Fits σx, σy and σz around each lysosome.
Radial Intensity
Computes radial profile and FWHM.
Final Radius
Combines both estimates into a robust radius.

## Slide 10
Detection Outputs
Coordinates
3D centroid
Diameter
Physical size
Volume
µm³
Peak Intensity
Maximum fluorescence
CSV Export
Publication-ready table
Overlay
Visual validation

## Slide 11
Cell Segmentation Pipeline
Cell Channel
Gaussian
Adaptive
Threshold
Morphology
Distance
Transform
Watershed
Labeled
Cells

## Slide 12
Lysosome Assignment
Input
Detected lysosomes + Cell labels
Decision
Inside cell? Overlap? Nearest cell?
Output
Cell ID Outside Serial IDs

## Slide 13
Signal Quantification
Cell Signal
Total fluorescence
Lysosome Signal
Integrated intensity
Cell Volume
Voxel count
Distance Analysis
0–0.2, 0.2–0.5 µm
Residual Signal
Outside puncta
Statistics
Per-cell CSV

## Slide 14
Napari Interactive Editing
Editable Objects
• Add/remove lysosomes • Change cell IDs • Mark outside/cell • Filter cells • Save edited tables
Workflow
Load results ↓ Inspect detections ↓ Manual correction ↓ Export corrected CSV

## Slide 15
Generated Outputs
lysosome_blobs_regions.csv
lysosomes_with_cell_vs_outside.csv
cell_signal_vs_lysosome_signal_extended.csv
Overlay TIFF stacks
MP4 / GIF videos
Debug masks
Final Deliverables
✓ Publication-ready tables ✓ Segmentation images ✓ Movies ✓ Quantitative statistics ✓ Napari-edited results

## Slide 16
Software Architecture
GUI
Image Loader
Metadata
Detection
Segmentation
Quantification
Visualization
Napari
Export

## Slide 17
Main Parameters
Detection
BLOB_THRESHOLD MIN/MAX_SIGMA
Segmentation
CH2_SMOOTH_SIGMA THRESH_BLOCK_SIZE ERODE_MULT
Watershed
DIST_SMOOTH_SIGMA H_MAXIMA
Classification
MARGIN_UM OVERLAP_ALPHA
Visualization
VIDEO_FPS NAPARI VIZ_MIN_VOXELS

## Slide 18
Repository Structure
README.md
requirements.txt
Lysosomes_Detector_GUI.py
Example images
Documentation
Output folder
Generated Outputs
CSV TIFF MP4 GIF Napari-edited tables Debug masks

## Slide 19
Installation
Quick Start
git clone <repository> pip install -r requirements.txt python Lysosomes_Detector_GUI.py Supports Python 3.12

## Slide 20
Future Developments
Deep learning segmentation
GPU acceleration
Batch processing
Parallel computing
Automatic report generation
Cloud processing
Plugin architecture
Multi-channel support